## Slide 2: Autonomous Vehicle Controls
Week 4
Cooperative adaptive cruise control

## Slide 3: Recap :
In the previous week we saw how to implement a level 2 adaptive cruise control (ACC) system ,also known as autonomous cruise control.
Implemented optimal control methods using LQR.
We also developed various levels of control which mimics actual production strategy.

## Slide 4: Learning objectives for this week
This week we will
  Try to improve the already built ACC system into an advance ACC system.
  Learn about a new cooperative adaptive cruise control which uses additional sensor set to improve ACC performance
  Implement this modified Adaptive cruise control into a simulation environment.

## Slide 5: Table of Contents:
Introduction to CACC
  Limitations of production ACC
  How can CACC help?
Control strategy for CACC
  Control strategy
  Spacing policy formulation
  CACC feed forward controller
Simulation and results
Notes: Imge1 : https://www.fhwa.dot.gov/publications/research/operations/15032/index.cfm

## Slide 6: Introduction to CACC

## Slide 7: Introduction to CACC
Cooperative Adaptive Cruise Control (CACC) is a longitudinal control method where an ACC system is supported by a V2V (vehicle to vehicle communication system).
Notes: Imag1 : https://www.eenewsautomotive.com/news/toyota-develops-its-own-automated-driving-technology
Imge2 : https://www.fhwa.dot.gov/publications/research/operations/15032/index.cfm

## Slide 8: Introduction to CACC
In addition to the radar and camera sensors used by the vehicle for ACC. The CACC system uses a wireless communication system to receive data from other target vehicles.
This technique has been developed for platooning and string stability in high traffic. We shall discuss them in further detail in the upcoming slides.

## Slide 9: String Stability & platooning
A platoon is a group of vehicles that travel together very close to each other with minimal risk of collision even at high speeds.
String stability
  It is the property of a string of vehicles by virtue of which the spacing error is guaranteed not to amplify as they propagate towards the end of the string.
Notes: Image1 ; https://www.drivingtests.co.nz/resources/what-is-vehicle-platooning/
Image 2- need to be recreated, instructor will provide specific instructions
Image 3 - instructor will recreate the image on matlab.

## Slide 10: String Stability & platooning
Eg: in a platoon of 6 cars. The error of spacing between the second and third cars do not amplify into an extremely large spacing error between the fifth and sixth car.

## Slide 11: Limitations of Adaptive cruise control
Traditional ACC systems suffer from a significant trade off between ride quality & spacing accuracy due to noise range and range rate signals.
ACC cannot be implemented at low time headway values as it would result in rear end collisions in case of sudden speed changes in the traffic (shock waves).

## Slide 12: Limitations of Adaptive cruise control
Due to radar / camera limitations, ACC does not do well in blind curves or hillcrest roads with target selection.
It is difficult to maintain string stability with traditional ACC if a constant spacing policy is used.

## Slide 13: How can CACC help?
CACC can help maintain a low time headway value i.e. the vehicles in the platoon will travel at much closer distances without risk of collision due to loss of string stability.

## Slide 14: How can CACC help?
Advantages
  More traffic throughput which increases the capacity of the road.
  With platooning there will be a reduction of air drag and prevention unnecessary acceleration & decelerations.
  CACC can also improve performance in blind curves where radar cannot detect targets.

## Slide 15: Control strategy for CACC

## Slide 16: CACC control strategy block diagram
Notes: Image created by instructor no modifications necessary

## Slide 17: Spacing policy formulation
∆xdesired=Vhost Thw+standstill distance where, Vhost is the host velocity , Thw is desired time headway and standstill distance is the gap to be maintained while stationary.
∆x=x1-x2-l
e= ∆x - ∆xdesired

## Slide 18: CACC feed forward controller
Feed forward formulation:
  F=Q (τs+1)/(T_hw s+1)
Where 1/τ represents the desired closed loop bandwidth.

## Slide 19: CACC controller implementation

## Slide 20: Simulation for CACC vs ACC

## Slide 21: Simulation results comparison between ACC and CACC

## Slide 22: Summary
CACC is a longitudinal control method where an ACC system is supported by a V2V
String stability is the property of a string of vehicles in which the spacing error are guaranteed not to amplify as they propagate towards the end of the string
CACC can help maintain a low time headway value i.e. the vehicles in the platoon will travel a much closer distances without danger for losing string stability

## Slide 23: THANK YOU